# Debug with aid of SPI interface
## Usage
- create a directory 'debugger' with 'debugger.h' in it
- zip the directory to debugger.zip
- //include library/add ZIP library within Arduino IDE
- //include library/debugger.h
- use the example to test
- documentation of SPI slave with LEONARDOs see kner.at
## Example
/* example for debug.h
* caveat: include SPI.h before include debugger.h
*
*/
#define DEBUG
#include <SPI.h>
#include <debugger.h>
void setup() {
beginDebug ();
}
void loop() {
TraceFunc (); // where am i?
Trace(F("here i am "));
Traceln2(13,HEX);
delay(1000);
}

## debugger.h
// Written by Nick Gammon
// September 2011
#ifndef Debugger_h
#define Debugger_h
#define SSS 13 //this pin number must be adapted to the external line connected to the spi master
#ifdef DEBUG
#define beginDebug() do { SPI.begin (); SPI.setClockDivider(SPI_CLOCK_DIV8); } while (0)
#define Trace(x) SPIdebug.print (x)
#define Trace2(x,y) SPIdebug.print (x,y)
#define Traceln(x) SPIdebug.println (x)
#define Traceln2(x,y) SPIdebug.println (x,y)
#define TraceFunc() do { SPIdebug.print (F("In function: ")); SPIdebug.println (__PRETTY_FUNCTION__); } while (0)
class tSPIdebug : public Print
{
public:
  virtual size_t write (const byte c)
    {
    digitalWrite(SSS, LOW);
    SPI.transfer (c);
    digitalWrite(SSS, HIGH);
    return 1;
    } // end of tSPIdebug::write
}; // end of tSPIdebug
// an instance of the SPIdebug object
tSPIdebug SPIdebug;
#else
#define beginDebug() ((void) 0)
#define Trace(x) ((void) 0)
#define Trace2(x,y) ((void) 0)
#define Traceln(x) ((void) 0)
#define Traceln2(x,y) ((void) 0)
#define TraceFunc() ((void) 0)
#endif
#endif