# 2.4′ TFT LCD Screen Module with TOUCH
http://www.elecfreaks.com/store/24-tft-lcd-tft0124-p-110.html

Bought in china in 2011; elder version of the display with ILI9325D controller; 3.3V version
This is a 3.3V LCD, so if you use it with a 5V platform like Arduino you'll need to convert pins to 3.3V
Test environment: arduino mega 2560 board (5V !) powered by usb cable

When controlling the display with arduino mega, the interface signals carry 4.2V!!! This leads to latchup at databus signals. The display flickers and stays white at the end.
Solution (quick and dirty!): since the setup and write operation to the tft registers works, there is a quick and dirty solution: after tft controller is set up, the databus is disabled by switching the arduino pins to input thus not driving any tft controller pins.
void deactivate_and_wait(){
  // set Databus inactive to prevent latchup
  for (int i = 22; i<=37; i++) pinMode(i,INPUT_PULLUP);
  delay(2000);
  for (int i = 22; i<=37; i++) pinMode(i,OUTPUT);
}

Solution (real solution) would be to use 3.3V interface (e.g. level shifter or resistor deviders)

UTFT library and examples: ILI9325D_16 Controller interface (Attention: there are tft displays with other drivers e.g. S6D1121
UTFT myGLCD(ILI9325D_16,38,39,40,41);
## Default pinout for UTFT Examples

        TFT	ARDUINO

RS	4	38
WR	5	39
CS	15	40
RESET	17	41
RD	6	3.3V
# Example with dirty solution (may destroy your display!)
// UTFT_Demo_320x240
// Copyright (C)2015 Rinky-Dink Electronics, Henning Karlsen. All right reserved
// web: http://www.RinkyDinkElectronics.com/
//
// This program is a demo of how to use most of the functions
// of the library with a supported display modules.
//
// This demo was made for modules with a screen resolution
// of 320x240 pixels.
//
// This program requires the UTFT library.
//

#include <UTFT.h>

// Declare which fonts we will be using
extern uint8_t SmallFont[];

// Set the pins to the correct ones for your development shield
// ------------------------------------------------------------
// Arduino Uno / 2009:
// -------------------
// Standard Arduino Uno/2009 shield : <display model>,A5,A4,A3,A2
// DisplayModule Arduino Uno TFT shield : <display model>,A5,A4,A3,A2
//
// Arduino Mega:
// -------------------
// Standard Arduino Mega/Due shield : <display model>,38,39,40,41
// CTE TFT LCD/SD Shield for Arduino Mega : <display model>,38,39,40,41
//
// Remember to change the model parameter to suit your display module!
UTFT myGLCD(5,38,39,40,41);

void setup()
{
  randomSeed(analogRead(0));

// Setup the LCD
  myGLCD.InitLCD();
  myGLCD.setFont(SmallFont);
}

void loop()
{
  int buf[318];
  int x, x2;
  int y, y2;
  int r;

// Clear the screen and draw the frame
  myGLCD.clrScr();

  myGLCD.setColor(255, 0, 0);
  myGLCD.fillRect(0, 0, 319, 13);
  myGLCD.setColor(64, 64, 64);
  myGLCD.fillRect(0, 226, 319, 239);
  myGLCD.setColor(255, 255, 255);
  myGLCD.setBackColor(255, 0, 0);
  myGLCD.print("* Universal Color TFT Display Library *", CENTER, 1);
  myGLCD.setBackColor(64, 64, 64);
  myGLCD.setColor(255,255,0);
  myGLCD.print("<http://www.RinkyDinkElectronics.com/>", CENTER, 227);

  myGLCD.setColor(0, 0, 255);
  myGLCD.drawRect(0, 14, 319, 225);

// Draw crosshairs
  myGLCD.setColor(0, 0, 255);
  myGLCD.setBackColor(0, 0, 0);
  myGLCD.drawLine(159, 15, 159, 224);
  myGLCD.drawLine(1, 119, 318, 119);
  for (int i=9; i<310; i+=10)
    myGLCD.drawLine(i, 117, i, 121);
  for (int i=19; i<220; i+=10)
    myGLCD.drawLine(157, i, 161, i);

// Draw sin-, cos- and tan-lines
  myGLCD.setColor(0,255,255);
  myGLCD.print("Sin", 5, 15);
  for (int i=1; i<318; i++)
  {
    myGLCD.drawPixel(i,119+(sin(((i*1.13)*3.14)/180)*95));
  }

  myGLCD.setColor(255,0,0);
  myGLCD.print("Cos", 5, 27);
  for (int i=1; i<318; i++)
  {
    myGLCD.drawPixel(i,119+(cos(((i*1.13)*3.14)/180)*95));
  }

  myGLCD.setColor(255,255,0);
  myGLCD.print("Tan", 5, 39);
  for (int i=1; i<318; i++)
  {
    myGLCD.drawPixel(i,119+(tan(((i*1.13)*3.14)/180)));
  }

  deactivate_and_wait();

  myGLCD.setColor(0,0,0);
  myGLCD.fillRect(1,15,318,224);
  myGLCD.setColor(0, 0, 255);
  myGLCD.setBackColor(0, 0, 0);
  myGLCD.drawLine(159, 15, 159, 224);
  myGLCD.drawLine(1, 119, 318, 119);

// Draw a moving sinewave
  x=1;
  for (int i=1; i<(318*20); i++)
  {
    x++;
    if (x==319)
      x=1;
    if (i>319)
    {
      if ((x==159)||(buf[x-1]==119))
        myGLCD.setColor(0,0,255);
      else
        myGLCD.setColor(0,0,0);
      myGLCD.drawPixel(x,buf[x-1]);
    }
    myGLCD.setColor(0,255,255);
    y=119+(sin(((i*1.1)*3.14)/180)*(90-(i / 100)));
    myGLCD.drawPixel(x,y);
    buf[x-1]=y;
  }

  deactivate_and_wait();

  myGLCD.setColor(0,0,0);
  myGLCD.fillRect(1,15,318,224);

// Draw some filled rectangles
  for (int i=1; i<6; i++)
  {
    switch (i)
    {
      case 1:
        myGLCD.setColor(255,0,255);
        break;
      case 2:
        myGLCD.setColor(255,0,0);
        break;
      case 3:
        myGLCD.setColor(0,255,0);
        break;
      case 4:
        myGLCD.setColor(0,0,255);
        break;
      case 5:
        myGLCD.setColor(255,255,0);
        break;
    }
    myGLCD.fillRect(70+(i*20), 30+(i*20), 130+(i*20), 90+(i*20));
  }

  deactivate_and_wait();

  myGLCD.setColor(0,0,0);
  myGLCD.fillRect(1,15,318,224);

// Draw some filled, rounded rectangles
  for (int i=1; i<6; i++)
  {
    switch (i)
    {
      case 1:
        myGLCD.setColor(255,0,255);
        break;
      case 2:
        myGLCD.setColor(255,0,0);
        break;
      case 3:
        myGLCD.setColor(0,255,0);
        break;
      case 4:
        myGLCD.setColor(0,0,255);
        break;
      case 5:
        myGLCD.setColor(255,255,0);
        break;
    }
    myGLCD.fillRoundRect(190-(i*20), 30+(i*20), 250-(i*20), 90+(i*20));
  }

  deactivate_and_wait();

  myGLCD.setColor(0,0,0);
  myGLCD.fillRect(1,15,318,224);

// Draw some filled circles
  for (int i=1; i<6; i++)
  {
    switch (i)
    {
      case 1:
        myGLCD.setColor(255,0,255);
        break;
      case 2:
        myGLCD.setColor(255,0,0);
        break;
      case 3:
        myGLCD.setColor(0,255,0);
        break;
      case 4:
        myGLCD.setColor(0,0,255);
        break;
      case 5:
        myGLCD.setColor(255,255,0);
        break;
    }
    myGLCD.fillCircle(100+(i*20),60+(i*20), 30);
  }

  deactivate_and_wait();

  myGLCD.setColor(0,0,0);
  myGLCD.fillRect(1,15,318,224);

// Draw some lines in a pattern
  myGLCD.setColor (255,0,0);
  for (int i=15; i<224; i+=5)
  {
    myGLCD.drawLine(1, i, (i*1.44)-10, 224);
  }
  myGLCD.setColor (255,0,0);
  for (int i=224; i>15; i-=5)
  {
    myGLCD.drawLine(318, i, (i*1.44)-11, 15);
  }
  myGLCD.setColor (0,255,255);
  for (int i=224; i>15; i-=5)
  {
    myGLCD.drawLine(1, i, 331-(i*1.44), 15);
  }
  myGLCD.setColor (0,255,255);
  for (int i=15; i<224; i+=5)
  {
    myGLCD.drawLine(318, i, 330-(i*1.44), 224);
  }

  deactivate_and_wait();

  myGLCD.setColor(0,0,0);
  myGLCD.fillRect(1,15,318,224);

// Draw some random circles
  for (int i=0; i<100; i++)
  {
    myGLCD.setColor(random(255), random(255), random(255));
    x=32+random(256);
    y=45+random(146);
    r=random(30);
    myGLCD.drawCircle(x, y, r);
  }

  deactivate_and_wait();

  myGLCD.setColor(0,0,0);
  myGLCD.fillRect(1,15,318,224);

// Draw some random rectangles
  for (int i=0; i<100; i++)
  {
    myGLCD.setColor(random(255), random(255), random(255));
    x=2+random(316);
    y=16+random(207);
    x2=2+random(316);
    y2=16+random(207);
    myGLCD.drawRect(x, y, x2, y2);
  }

  deactivate_and_wait();

  myGLCD.setColor(0,0,0);
  myGLCD.fillRect(1,15,318,224);

// Draw some random rounded rectangles
  for (int i=0; i<100; i++)
  {
    myGLCD.setColor(random(255), random(255), random(255));
    x=2+random(316);
    y=16+random(207);
    x2=2+random(316);
    y2=16+random(207);
    myGLCD.drawRoundRect(x, y, x2, y2);
  }

  deactivate_and_wait();

  myGLCD.setColor(0,0,0);
  myGLCD.fillRect(1,15,318,224);

  for (int i=0; i<100; i++)
  {
    myGLCD.setColor(random(255), random(255), random(255));
    x=2+random(316);
    y=16+random(209);
    x2=2+random(316);
    y2=16+random(209);
    myGLCD.drawLine(x, y, x2, y2);
  }

  deactivate_and_wait();

  myGLCD.setColor(0,0,0);
  myGLCD.fillRect(1,15,318,224);

  for (int i=0; i<10000; i++)
  {
    myGLCD.setColor(random(255), random(255), random(255));
    myGLCD.drawPixel(2+random(316), 16+random(209));
  }

  deactivate_and_wait();

  myGLCD.fillScr(0, 0, 255);
  myGLCD.setColor(255, 0, 0);
  myGLCD.fillRoundRect(80, 70, 239, 169);

  myGLCD.setColor(255, 255, 255);
  myGLCD.setBackColor(255, 0, 0);
  myGLCD.print("That's it!", CENTER, 93);
  myGLCD.print("Restarting in a", CENTER, 119);
  myGLCD.print("few seconds...", CENTER, 132);

  myGLCD.setColor(0, 255, 0);
  myGLCD.setBackColor(0, 0, 255);
  myGLCD.print("Runtime: (msecs)", CENTER, 210);
  myGLCD.printNumI(millis(), CENTER, 225);

  deactivate_and_wait();
}

void deactivate_and_wait(){
  // set Databus inactive to prevent latchup
  for (int i = 22; i<=37; i++) pinMode(i,INPUT_PULLUP);
  delay(2000);
  for (int i = 22; i<=37; i++) pinMode(i,OUTPUT);
}

# Touch
utouch Library
//tclk, byte tcs, byte tdin, byte dout, byte irq
UTouch myTouch( 6, 5, 4, 3, 2);

Connections:
Name Display Arduino Mega
clk	29	6
cs	30	5
din 31	4
dout	33	3
irq	34	2